## Slide 1: Manufacturing Processes
By
Sachin Gupta

## Slide 2: Introduction
Manufacturing is the backbone of any industrialized nation.
Manufacturing and technical staff in industry must know the various manufacturing processes, materials being processed, tools and equipments for manufacturing different components or products with optimal process plan using proper precautions and specified safety rules to avoid accidents.
Beside above, all kinds of the future engineers must know the basic requirements of workshop activities in term of man, machine, material, methods, money and other infrastructure facilities needed to be positioned properly for optimal shop layouts or plant layout and other support services effectively adjusted or located in the industry or plant within a well-planned manufacturing organization.

## Slide 3: Importance
Manufacturing is achieved through a proper planning and control system.
It is classified as continuous production and intermittent production.
Continuous production involves a continuous flow of material physically, leading to large quantities of finished good.
Chemical processing, cigarette manufacturing and cement manufacturing are some of the industries employing continuous production.
Also, sheets, wires, pipes, TV sets, motor cycles are examples of continuous production.
An intermitted production involves interrupted flow of material through the plant.
Machine shops, welding shops, etc. are industries employing intermittent production.

## Slide 4
Manufacturing is backbone of any economy.
Manufacturing industries provides employment to hundreds of people.
Before the industrial revolution, manufacturing was carried out in rural area, where household-based manufacturing was the trend.
Later government policy and entrepreneurs organized a number of manufacturing house hold in to a single enterprise producing goods at large scale.
It leads to development of industrialization and society.
Manufacturing provides an opportunity for establishment of allied industries

## Slide 5: Classifications
For producing of products materials are needed. It is therefore important to know the characteristics of the available engineering materials.
Raw materials used manufacturing of products, tools, machines and equipments in factories or industries are extracted from ores.
The ores are suitably converted the metal into a molten form by reducing or refining processes in foundries.
This molten metal is poured into moulds for providing commercial castings, called ingots.

## Slide 7: PRIMARY SHAPING PROCESSES
Primary shaping processes are manufacturing of a product from an amorphous material.
Some processes produces finish products or articles into its usual form whereas others do not, and require further working to finish component to the desired shape and size.
Castings need re-melting of scrap and defective ingots in cupola or in some other melting furnace and then pouring of the molten metal into sand or metallic moulds to obtain the castings. Thus the intricate shapes can be manufactured.
Typical examples of the products that are produced by casting process are machine beds, automobile engines, carburetors, flywheels etc. The parts produced through these processes may or may not require to under go further operations.
Some of the important primary shaping processes is:
(1) Casting, (2) Powder metallurgy, (3) Plastic technology, (4) Gas cutting, (5) Bending and (6) Forging.

## Slide 8: SECONDARY OR MACHINING PROCESSES
As a large number of components require further processing after the primary processes. These components are subjected to one or more machining operations in machine shops, to obtain the desired shape and dimensional accuracy on flat and cylindrical jobs. Thus, the components undergoing these operations are the roughly finished products received through primary shaping processes.
The process of removing the undesired or unwanted material from the workpiece or job or component to produce a required shape using a cutting tool is known as machining. This can be done by a manual process or by using a machine called a machine tool (traditional machines namely lathe, milling machine, drilling, shaper, planner, slotter).

## Slide 9: Classification of Manufacturing Processes

## Slide 10: METAL FORMING PROCESSES
Forming processes encompasses a wide variety of techniques, which make use of suitable force, pressure or stresses, like compression, tension and shear or their combination to cause a permanent deformation of the raw material to impart required shape. These processes are also known as mechanical working.
Such processes lead to production of directly usable articles which include kitchen utensils, rods, wires, rails, cold drink bottle caps, collapsible tubes etc. Some of the important metals forming processes are:

## Slide 11
Hot working Processes
(1) Forging, (2) Rolling, (3) Hot spinning, (4) Extrusion, (5) Hot drawing and
Cold working processes
(1) Cold forging, (2) Cold rolling, (3) Cold heading, (4) Cold drawing, (5) Wire drawing, (6) Stretch forming, (7) Sheet metal working processes such as piercing, punching, coining, deep drawing, bending etc.

## Slide 12: JOINING PROCESSES
These processes are used for assembling metal parts and in general fabrication work. Such requirements usually occur when several pieces are to be joined together to fabricate a desired structure of products.
These processes are used for developing water-tight joints. Temporary, semi permanent or permanent type of fastening to make a good joint is generally created by these processes.
Temporary joining of components can be achieved by use of nuts, screws and bolts. Adhesives are also used to make temporary joints. Some of the important and common joining processes are:
(1) Welding (plastic or fusion), (2) Brazing, (3) Soldering, (4) Riveting, (5) Screwing, (6) Press fitting, (7) Adhesive bonding, (8) Nut and bolt joints.

## Slide 13: SURFACE FINISHING PROCESSES
Surface finishing processes are utilized for imparting intended surface finish on the surface of a job.
By imparting a surface finishing process, dimension of part is not changed functionally; either a very negligible amount of material is removed from the certain material is added to the surface of the job.
These processes should not be misunderstood as metal removing processes in any case as they are primarily intended to provide a good surface finish or a decorative or protective coating on to the metal surface.
Surface cleaning process also called as a surface finishing process. Some of the commonly used surface finishing processes are:
Super finishing, Polishing Electroplating, Metal spraying, Painting, Metallic coating

## Slide 14: PROCESSES EFFECTING CHANGE IN PROPERTIES
Processes effecting change in properties are generally employed to provide certain specific properties to the metal work pieces for making them suitable for particular operations or use.
Some important material properties like hardening, softening and grain refinement are needed to jobs and hence are imparted by heat treatment. Heat treatments affect the physical properties and also make a marked change in the internal structure of the metal.
Similarly the metal forming processes effect on the physical properties of work pieces. A few such commonly used processes are given as under:
(1) Annealing, (2) Normalising, (3) Hardening, (4) Tempering